##### PLL Board Pin out: 
(20-pole header on PLL board)

##### 1_ gnd
2_ gnd
3_ gnd
4_ gnd
5_ +5V
6_ +5V
7_ Clk (I^2Cbus)
8_ NC
9_ NC10_ DATA (I^2Cbus)
11_ YIG on/off*) 
12_ LE (I^2Cbus)
13_ NC 
14_ FO/LD output of LMX chip
15_ +8.5V 
16_ +8.5V
17_ GND 
18_ GND
19_ 10MHz. ref. out
20_ Tune Ref. 0-2.5V

NOTE: 20 Pin header is included. 
*) connect 5V via 1kOhm to pin 11 for YIG on.

#### YIG output pinout (small white header extending from board)

#### Pin 1 is on the right in the top view, left side of image)

#### 1 Red +Vcc
2 Black GND
3 Violet YIG  Tuning Coil+
4 Orange YIG Tuning Coil-
5 Yellow YIG Modulation Coil
6 Gray YIG  Modulation Coil